## Slide 1
Exp-5
RJEs: Remote job entry points
Design a circuit for a 3-bit register that has 2-bit control inputs and performs the following operations:
                A B OPERATION
                1 1 Load parallel Data
                0 1 Circular Right Shift
                1 0 Circular Left Shift
Use D-flip flops and 4:1 MUX to design the circuit. Observe the output on LEDs. Use clock freq of 1 Hz from signal generator.